## Slide 1
CHAPTER 2
NUMBER SYSTEMS,
OPERATIONS,
AND CODES
数字系统、运算和编码

## Slide 2
2-1 DECIMAL NUMBERS
十进制数

## Slide 3
Decimal（十进制） Review
 Numbers(数) consist of a bunch of digits（数字）, each with a
weight（权重）.
1
6
2
.
3
7
5
Digits
100 10 1
1/10 1/100 1/1000 Weights
• These weights are all powers of the base, which is 10. We can
rewrite this:
1
6
2
.
3
7
5
Digits
2
1
0
-1
-2
-3
10 10 10
10 10 10 Weights
• To find the decimal value of a number, multiply each digit by its
weight and sum the products.
×
2 + × 1 + × 0 + × -1 + × -2 + × -3 =
1 10 6 10 2 10 3 10 7 10 5 10 162.375

D
=
k *10i
i

## Slide 4
Nothing Special about 10!
 Decimal system (and the idea of “0”) was invented in
India around 100-500AD.
 Why did they use 10? Anything special about it?
 Not really.
 Probably the fact that we have 10 fingers influenced this.
 Will a base other than 10 work?
 Sure.
345 in base 9 3 9 4 9 5 9 284 in base 10
= × 2 + × 1 + × 0 =
• What about base 2?

=
ki * N
i
D

## Slide 5
2-2 BINARY NUMBERS
二进制数

## Slide 6
Introductory Paragraph
 The binary number system is simply another way
to represent quantities.
 A binary number is a weighted number（加权
数）.
 The decimal system with its ten digits is a base-
ten system; the binary system with its two
digits is a base-two system. The two digits (bits)
are 1 and 0. The position of a 1 or 0 in a binary
number indicates its weight, or value within the
number, just as the position of a decimal digit
determines the value of that digit. The weights
in a binary number are based on powers of two.

## Slide 7
Introductory Paragraph
 The binary system is less complicated than
the decimal system because it has only two
digits. It may seem more difficult at first
because it is unfamiliar to you.

## Slide 8
The Weighting Structure of Binary Numbers
 The right-most bit is the LSB（最低有效位 least
significant bit） in a binary whole number and has a
weight of 20=1. The weights increase from right to left
by a power of two for each bit. The left-most bit is the
MSB（最高有效位 most significant bit）.
 Fractional numbers（小数） can also be represented in
binary by placing bits to the right of the binary point.
The left-most bit is the MSB in a binary fractional
number and has a weight of 2-1=0.5. The fractional
weights decreases from left to right by a negative
power of two for each bit.

## Slide 10
Counting in Binary
 A binary count of 0 through 15 is shown below. As
you will see, 4 bits are required to count from 0 to
15.

## Slide 11
Binary-to Decimal Conversion
 The decimal value of any binary number can be
found by adding the weights of all bits that are 1
and discarding the weights of all bits that are 0.
145

D
=
ki * N
i

## Slide 12
2-3 DECIMAL-TO-BINARY
CONVERSION

## Slide 13
Repeated Division-by-2 Method
 A systematic method of converting whole numbers
from decimal to binary is the repeated devision-by-
2 process.
39?
10 0111

## Slide 14
Repeated Multiplication-by-2 Method
 A systematic method of converting fractional
numbers from decimal to binary is the repeated
multiplication-by-2 process.
0.010101000111101…
0.33=?

## Slide 15
2-4 BINARY ARITHMETIC

## Slide 16
Binary Addition
 The four basic rules for adding binary digits (bits)
are as follows:
0 + 0 = 0 Sum of 0 with a carry of 0
0 + 1 = 1 Sum of 1 with a carry of 0
1 + 0 = 1 Sum of 1 with a carry of 0
1 + 1 = 0 Sum of 0 with a carry of 1
• [Example] Add 1111 and 1100.
1 1 1 1
1 1 00
+
11011
1 1 01 1

## Slide 17
Binary Subtraction
 The four basic rules for subtraction binary digits
(bits) are as follows:
0 - 0 = 0 Difference of 0 with a borrow of 0
0 - 1 = 1 Difference of 1 with a borrow of 1
1 - 0 = 1 Difference of 1 with a borrow of 0
1 - 1 = 0 Difference of 0 with a borrow of 0
• [Example] Subtract 100 from 111.
1 1 1
111-100=11
1 00
1 1
−

## Slide 18
Binary Multiplication
 The four basic rules for multiplication binary digits
(bits) are as follows:
0×0 = 0
0×1= 0
1×0 = 0
1×1=1
1 1 0 1
1 0 1 0
×
• [Example] Multiply 1101 by 1010.
1 1 0 1
1 1 0 1
1 0 0 0 0 0 1 0

## Slide 19
Binary Division
 Division in binary follows the same procedure as
division in decimal.
• [Example] Divide 1100 by 100.
1 1
1 0 0
1 1 0 0
1 0 0
1 0 0
1 0 0
0

## Slide 20
2-5 SIGNED NUMBERS
带符号数

## Slide 21
The Sign Bit（符号位）
 The left-most bit in a signed binary number is the
sign bit, which tells you whether the number is
positive（正） or negative（负）. A 0 is for positive,
and a 1 is for negative.

## Slide 22
2.5.1 Sign-Magnitude(符号-幅值) System
 When a signed binary number is represented in
sign-magnitude, the left-most bit is the sign bit and
the remaining bits are the magnitude bits. The
magnitude bits are in true (uncomplemented（非补
码）) binary for both positive and negative numbers.
Sign bit
Sign bit


0 0 011001
1 0011 001


Magnitude bits
Magnitude bits
+25
−25
• The decimal values are determined by summing the
weights in all the magnitude bit positions where
there are 1s. The sign is determined by examination
of the sign bit.

## Slide 23
Sign-Magnitude System
 [Example 2-15] Determine the decimal value of this
signed binary number expressed in sign-magnitude:
10010101.
Solution.
Summing the weights in all the magnitude bit positions
where there are 1s,
2 2 2 21
4 + 2 + 0 =
The sign bit is 1; therefore, the decimal number is - 21.

## Slide 24
2.5.2 The Complement System of
Binary Numbers
1’s complement and
2’s complement

## Slide 25
Finding the 1’s Complement of a Binary Number
 The 1’s complement (补码/反码) of a binary number is
found by changing all 1s to 0s and all 0s to 1s.

## Slide 26
Definition of 1’s Complement
number
 Positive numbers in the 1’s complement system are
represented the same way as the positive sign-
magnitude numbers.
 Negative numbers, however, are the 1’s
complements of the corresponding positive numbers.
00011001
111001 10
+25
−25

## Slide 27
Conversion from a 1’s Complement
number to decimal
 The decimal values of positive numbers are determined
by summing the weights in all bit positions where there
are 1s.
 The decimal values of negative numbers are determined
by summing the weights in all bit positions where there
are 1s, and adding 1 to the result. The weight of the sign
bit is given a negative value.

## Slide 28
1’s Complement System
 [Example 2-16] Determine the decimal value of the
signed binary numbers expressed in 1’s complement:
(a) 00010111 (b) 11101000.
Solution.
(a) Summing the weights in all the magnitude bit positions
where there are 1s,
2 2 2 2 23
4 + 2 + 1 + 0 = +
(b) Summing the weights in all the magnitude bit positions
where there are 1s,
− 7 + 6 + 5 + 3 = −
2 2 2 2 24
Adding 1 to the result
- 24 +1= -23

## Slide 29
1’s Complement System
 Why?
00011001
11100110
+25
−25
1110 0110 =
=1 0000 0000 −1− 00011001
− 00011001=1110 0110 −1 0000 0000 +1
=1000 0000 +110 0110 −1 0000 0000 +1
2 2 2 2 2 1
= − 7 + 6 + 5 + 2 + 1 +

## Slide 30
2’s Complement of a Binary Number
 The 2’s complement（补）of a binary number is found by
adding 1 to the LSB of the 1’s complement.

## Slide 31
2’s Complement System
 Positive numbers in the 2’s complement system are
represented the same way as in sign-magnitude and
1’s complement systems.
 Negative numbers are the 2’s complements of the
corresponding positive numbers.
00011001
11100111
 
 
+25
−25

## Slide 32
Conversion from a 2’s Complement
number to decimal
• The decimal values are determined by summing the
weights in all bit positions where there are 1s. The
weight of the sign bit is given a negative value.

## Slide 33
2’s Complement System
 [Example 2-17] Determine the decimal value of the
signed binary numbers expressed in 2’s complement:
(a) 01010110 (b) 10101010.
Solution.
(a) Summing the weights in all the magnitude bit positions
where there are 1s,
2 2 2 2 86
6 + 4 + 2 + 1 = +
(b) Summing the weights in all the magnitude bit positions
where there are 1s,
2 2 2 2 86
− 7 + 5 + 3 + 1 = −

## Slide 34
The 2's complement of an n-bit number x is defined by
x ≥ 0
 x,
[x]2c =

n
+
<
2 x, x 0

For n = 8, we have
[0000 0000]2c = 0000 0000
[0000 0001]2c = 0000 0001
[0000 0010]2c = 0000 0010

[0111 1111]2c = 01111111

## Slide 35
and
[−0000 0001]2c =1 0000 0000 − 0000 0001
= (1+1111 1111) − 0000 0001
= (11111111− 0000 0001) +1
=11111110 +1
=11111111
[−0000 0010]2c =1 0000 0000 − 0000 0010
= (1+1111 1111) − 0000 0010
= (11111111− 0000 0010) +1
=11111101+1
=11111110


## Slide 36
2’s Complement Advantage
 To convert to decimal
 The 2’s complement system simply requires a
summation of weights regardless of whether
the number is positive or negative.
(在二进制转十进制的计算中，采用2的补码形式表示
的数字，不管是正数还是负数仅需要一个统一的权重
求和的计算方式就可以实现)
 The sign-magnitude system requires two steps –
sum the weights of the magnitude bits and
examine the sign bit to determine if the
number is positive or negative.
(而采用’符号-幅值’表示形式则需要两个步骤——（1）
对幅值表示部分进行权重求和；（2）判断符号位是正
还是负)

## Slide 37
2’s Complement Advantage
 The 1’s complement system requires adding 1 to
the summation of weights for negative numbers
but not for positive numbers.
(1的补码形式表示的二进制数，对于负数需要在最后的
结果进行加1，对于正数则不需要，因此无法实现计算
算法的统一)
 Also, the 1’s complement system is not used
because two representations of zero
(00000000 or 11111111) are possible.
(1的补码形式另一个缺陷，零的表示有两种表示
（ 00000000 or 11111111 ），表达形式不唯一)

## Slide 38
Range of Signed Integer Numbers
 The number of different combinations of n bits is
Total combinations 2n
=
• For 2’s complement signed numbers, the range of
value for n-bit numbers is
−
2 to (2 1)
n−1
n−1
−
• For 1’s complement signed numbers, the range of
value for n-bit numbers is
−
n−1 + to
2 1
(2 1)
n−1
−
负数比上面多减了一个0

## Slide 39
Floating-Point Numbers（浮点数）
 To represent very large numbers, many bits are
required.
 The floating-point number, based on scientific
notation, is capable of representing very large or
very small numbers without increasing the number of
bits.（模仿科学计数法）
 A floating-point number consists of two parts:
Mantissa(定点尾数) and Exponent(指数)
32 bit
Single-Precision
Floating-Point
Binary Number
S
Exponent (E)
Mantissa (fraction, F)
1bit
8 bits
23 bits

## Slide 40
Floating-Point Numbers（浮点数）
 Example: 1011010010001 (5777) = 1. 011010010001 x 2^12
32 bit
01101001000100000000000
0
10001011
1bit
8 bits
23 bits
 Mantissa: the left-most bit ‘1’ is understood to be there
although it does not occupy an actual bit position. So
effectively, there are 24 bits in the mantissa.（个位的1省略不写）
 Exponent(1~255): it is a biased exponent which is obtained by
adding 127 to the actual exponent. So the range of an actual
exponent values from -126 to +128.转化为正数省去了signed bit

## Slide 41
Floating-Point Numbers（浮点数）
 两个特殊数字：0.0 is represented by 0s
32 bit
0
00000000000000000000000
0
00000000
1bit
8 bits
23 bits
 Infinity(无穷大) is represented by all 1s in the exponent and all
0s in the mantissa.
32 bit
INF
00000000000000000000000
0
11111111
1bit
8 bits
23 bits

## Slide 42
 The 8-bit grouping has been given the special name byte.
Bit Grouping Name
8-bit
Byte
16-bit
32-bit
Word
Double word
/ float number

## Slide 43
2-6 ARITHMETIC
OPERATIONS WITH SIGNED
NUMBERS
带符号数的算术运算

## Slide 44
Addition（加法）
 The two numbers in an addition are the augend（被
加数） and the addend（加数）. The results are the
sum （和）and the carry（进位）.
[x + y] = [x] +[y]
2c
2c
2c
• The addition process is stated as follows: add the
two numbers and discard any final carry bit.

## Slide 45
Overflow Condition（溢出条件）
 When two numbers are added and the number of
bits required to represent the sum exceeds the
number of bits in the two numbers, an overflow
results as indicated by an incorrect sign bit.
 An overflow can occur only when both numbers are
positive or both numbers are negative.
• [Example]
(a) 01111101(125) + 00111010(58) =10110111(183) ?
(b) 10001000 + 11101101 = ?

## Slide 46
Subtraction（减法）
 The two numbers in a subtraction are the minuend
（被减数） and the subtrahend（减数）. The results
are the difference（差） and the borrow（借位）.
[x − y] = [x + (−y)] = [x] +[−y]
2c
2c
2c
2c
minuend
substrahend
• The subtraction process is stated as follows: take
the 2’s complement of the subtrahend and add.
Discard any final carry bit.
• [Example]
(a) 0001000 - 00000011 = ?
(b) 11100111 - 00010011 = ?

## Slide 48
Multiplication（乘法）
 The two numbers in a multiplication are the
multiplicand（被乘数）and the multiplier（乘数）.
The result is the product（积）.
• The multiplication operation in most computers is
accomplished using partial product method（部分积方
法）. The basic steps in the process are as follows:
– Determine if the signs of the two numbers are the same.
This determines what the sign of the product will be.
– Change any negative number to true (uncomplemented) form.
– Starting with the LSB of the multiplicand, generate the
partial products. Shift each successive partial product one
bit to the left.
– Add each partial product to the sum of the previous partial
products to get the final product.
– If the sign of the product is negative, take the 2’s
complement of the product. Attach the sign bit to the
product.

## Slide 51
Division （除法）
 The two numbers in a division are the dividend（被
除数） and the divisor（除数）. The results are the
quotient（商） and the remainder（余数）.
• The basic steps in a division the process are as
follows:
– Determine if the signs of the two numbers are the same.
This determines what the sign of the quotient will be.
– Change any negative number to true (uncomplemented) form.
– Initialize the quotient to zero and initialize the partial
remainder to the dividend.
– Subtract the divisor from the partial remainder using 2’s
complement addition to get the next partial remainder. If
the result is positive, add 1 to the quotient and repeat for
the next partial remainder; otherwise, the division is
complete.

## Slide 54
Division
 [Example 2-23] Divide 01100100（100） by
00011001（25）
 [Example 2-23a] Divide 01100100（100） by
00011010（26）
 [Example 2-23b] Divide 01100100（100） by
11100111（-26）
 [Example 2-23c] Divide 10011100（-100） by
00011010 （+26）
 [Example 2-23d] Divide 10011100（-100） by
11100111 （-26）

## Slide 55
2-8 HEXADECIMAL
NUMBERS（十六进制数）

## Slide 56
Why Hexadecimal?
 As you are probably aware, long binary numbers are
difficult to read and write because it is easy to
drop or transpose a bit. Since computers and
microprocessors understand only 1s and 0s, it is
necessary to use these digits when you program in
machine language.
 用二进制来表示一个数字需要占用较多的位数，书写起
来较为麻烦，容易出错。但是计算机系统中只能识别0
和1两个数字，因此在计算机的实际执行代码中必须采
用二进制。

## Slide 57
Why Hexadecimal?
 The hexadecimal number system has 16 digits and is
used primarily as a compact way of displaying or
writing binary numbers because it is very easy to
convert between binary and hexadecimal.
 十六进制数具有16个数字，是一种高效紧凑表示二进制
数的一种技术方法，同时十六进制数和二进制数之间的
转换也非常方便。
 10 numeric digits (0, 1, 2, 3, 4, 5, 6, 7, 8, 9) and 6
alphabetic characters (A, B, C, D, E, F) make up the
hexadecimal number system.

## Slide 58
Relationship between hexadecimal and binary
 Each hexadecimal digit represents a 4-bit binary
number.

## Slide 59
Binary-to-Hexadecimal Conversion
 Very straightforward! Simply break the binary number into
4-bit groups, starting at the right-most bit and replace each
4-bit group with the equivalent hexadecimal symbol.

## Slide 60
Hexadecimal-to-Binary Conversion
 Very straightforward! Simply replace each hexadecimal
symbol with the equivalent 4-bit group.

## Slide 61
Hexadecimal-to-Decimal Conversion
 Multiply the decimal value of each hexadecimal digit by its
weight and then take the sum of these products.

## Slide 62
Decimal-to-Hexadecimal Conversion
 Repeated division of a decimal number by 16 will
produce the equivalent hexadecimal number.
 [Example 2-28] Convert the decimal number 650 to
hexadecimal by repeated division by 16.
LSB
MSB

## Slide 63
2-9 BINARY CODED DECIMAL (BCD)

## Slide 64
Introductory Paragraph
 Binary coded decimal (BCD) is a way to express each
of the decimal digits with a binary code. Since
there are only ten code groups in the BCD system,
it is very easy to convert between decimal and BCD.
Because we like to read and write in decimal, the
BCD code provides an excellent interface to binary
systems. Examples of such interfaces are keypad
inputs and digital readouts.

## Slide 65
The 8421 Code
 The 8421 code is a type of BCD code.
 BCD means that each decimal digit, 0 through 9, is
represented by a binary code of four bits.
• The designation 8421 indicates the binary weights of
the four bits.
• 1010, 1011, 1100, 1101, 1110, and 1111 are invalid codes.
• The 8421 code is the predominant BCD code, and
when we refer to BCD, we always mean the 8421 code
unless otherwise stated.

## Slide 68
BCD Addition
 BCD is a numerical code and can be used in
arithmetic operations. Here is how to add two BCD
numbers:
 Add the two BCD numbers, using the rules for binary
addition.
 If a 4-bit sum is equal to or less than 9, it is a valid BCD
number.
 If a 4-bit sum is greater than 9, or if a carry out of the
4-bit group is generated, it is an invalid result. Add 6
(0110) to the 4-bit sum in order to skip the six invalid
codes and returned the code to 8421. If a carry results
when 6 is added, simply add the carry to the next 4-bit
group.

## Slide 71
2-10 DIGITAL CODES AND PARITY
数字编码和奇偶校验

## Slide 72
The Gray Code（格雷码）
 The Gray code is unweighted and is not an
arithmetic code; that is, there are no specific
weights assigned to the bit positions.
 The important feature of the Gray code is that it
exhibits only a single bit change from one code
number to the next.相邻码

## Slide 74
Binary-to-Gray code Conversion
 The MSB in the Gray code is the same as the
corresponding MSB in the binary number.
 Going from left to right, add each adjacent pair of binary
code bits to get the next Gray code bit. Discard carries.

## Slide 75
Gray-to-Binary Conversion
 The MSB in the binary code is the same as the
corresponding MSB in the Gray code.
 Going from left to right, add each binary code bit
generated to the Gray code bit in the next adjacent
position. Discard carries.

## Slide 76
Application Example
 A simplified diagram of a 3-bit shaft position
encoder mechanism（三位轴角位置编译器） is shown
below.

## Slide 78
Application Example
 Consider what happens if one brush (for example,
the MSB brush) is slightly ahead of the others
during the transition from one sector to the next.

## Slide 79
Alphanumeric Codes（字母数字编码）
 In the strictest sense, alphanumeric codes are
codes that represent numbers and alphabetic
characters (letters). Most such codes, however,
also represent other characters such as symbols
and various instructions necessary for conveying
information. The ASCII is the most common
alphanumeric code.
 ASCII has 128 characters represented by a 7-bit
binary code.
 The first 32 are nongraphic characters (control
characters). That are never printed or displayed and
used only for control purposes.
 The others are graphic characters that can be printed or
displayed and include the letters of the alphabet
(lowercase and uppercase), the ten decimal digits,
punctuation signs, and other commonly used symbols.

## Slide 80
ASCII Code

## Slide 81
Parity Method for Error Detection
 Many systems use a parity bit as a means for bit error
detection.
 Any group of bits contain either an even or an odd number
of 1s. A parity bit is attached to a group of bits to make the
total number of 1s in a group always even or always odd. An
even/odd parity bit makes the total number of 1s even/odd.

## Slide 84
Parity Method for Error Detection
 A parity bit provides for the detection of a single bit error (or
any odd number of errors, which is very unlikely) but cannot
check for two errors in one group.

## Slide 94
Homework
 Problems: 6(c,e,g), 7(b,e), 9(h), 13(h), 14(b)(保留
小时后6位), 16(e,f), 17(d), 18(b), 22(h), 23(c)(d),
24(c)(d), 25(c)(d), 28(a)(b), 34(b), 37(g), 38(f),
39(g), 40(g), 42(b), 44(g), 47(k), 50(h), 52(f), 56(c),
57(c), 58.